## Slide 1
System-Level Evaluation of the N-way Fused MX Dot-Product PE
SCALE-Sim system-level simulation + PrimeTime PX synthesis results

## Slide 2
SCALE-Sim Configuration
configs/mx_fused_pe_32x32_os.cfg
▸ Array size: 32 x 32 (1024 PEs) -- 1 SCALE-Sim PE = 1 instance of the fused N-way dot-product unit
▸ Dataflow: Output-Stationary (OS)
- Chosen to match the PE's internally-accumulating output register: partial sums held and
- updated locally within each PE, mirroring the double-pumped accumulator's behavior
▸ On-chip SRAM: 64 KB each for IFMAP / Filter / OFMAP
▸ Bandwidth: nominal 10 words/cycle, InterfaceBandwidth = CALC
- SCALE-Sim estimates whatever bandwidth avoids stalling compute, rather than enforcing a cap
- -> this is why every evaluated workload reports zero stall cycles (compute-bound throughout)
▸ Sparsity support: disabled
▸ Per-PE compute model: SCALE-Sim natively assumes 1 op/PE/cycle (no notion of precision or fusion width N)
Same configuration used for every workload in this evaluation; restated at the top of both result text files for self-containment.

## Slide 3
Raw SCALE-Sim Results
mx_pe_eval_raw_metrics.csv -- synthesis-independent, N-independent
Workload | Layers | Total MACs | Cycles (N=1 baseline) | Stall cycles
ResNet-18 | 21 | 1,471,181,568 | 1,718,353 | 0
AlexNet | 5 | 805,118,496 | 850,960 | 0
Transformer-Fwd | 54 | 5,826,038,528 | 7,133,750 | 0
Transformer-InpGrad | 54 | 4,089,184,256 | 5,899,178 | 0
MLPerf-Transformer * | 891 | 113,029,120 | 4,870,117 | 0
ViT-S | 5 | 275,165,184 | 352,781 | 0
ViT-B | 5 | 983,248,896 | 1,169,093 | 0
ViT-L | 5 | 1,761,378,304 | 2,071,105 | 0
ViT-H | 5 | 3,601,858,560 | 3,711,547 | 0
ViT-bigG | 4 | 1,555,562,496 | 1,611,004 | 0
* MLPerf-Transformer decomposes attention into ~890 narrow per-head GEMMs -- kept for completeness, treated as an outlier below (see slide 4).

## Slide 4
Post-Processing Methodology
Mapping SCALE-Sim's baseline (N=1) simulation to the fused N-way design
▸ SCALE-Sim has no native notion of operand precision or per-PE reduction width
- -> each workload is simulated once, unmodified, to get baseline per-layer cycles C_l and stall cycles S_l
▸ Fused-N cycle projection (per layer, before summing):
- C_l(N) = S_l + ceil( (C_l - S_l) / N )
- stall cycles preserved unchanged -- memory traffic is independent of the PE's fusion width
▸ Cycles -> latency -> throughput, using the post-synthesis clock period T(N):
- Latency(N) = C(N) x T(N) Achieved TOPS(N) = 2 x MACs / Latency(N)
- Peak TOPS(N) = 2 x N x 1024 x (1/T(N))
▸ Power / area (not modeled by SCALE-Sim) from post-synthesis per-PE figures:
- Power_array(N) = Power_PE(N) x 1024 Area_array(N) = Area_PE(N) x 1024 / 1e6
▸ Two decoupled stages: (1) raw metrics extraction [synthesis-independent] -> (2) PPA recompute
- [synthesis-dependent] -- stage 2 reruns with new synthesis numbers, no SCALE-Sim re-run needed

## Slide 5
SCALE-Sim-Only Findings
Before combining with synthesis results
▸ Realized fusion speedup is exact, not just theoretical, on every evaluated workload:
- 4.00x (N=4) / 8.00x (N=8) / 16.00x (N=16) -- vs. a same-clock, unfused (N=1) reference
- Follows directly from zero stall cycles everywhere: every workload is compute-bound end-to-end,
- so the full theoretical fusion benefit is realized, not partially masked by memory stalls
▸ Array utilization range across evaluated workloads: 67.7% - 94.8%
- (excludes the MLPerf-Transformer benchmark artifact -- see slide 2)
▸ Same-workload comparison vs. Cuyckens et al. NPU-integrated tensor core (8x8, 64 MACs):
- ResNet-18 (inference): 83.6% vs. 99.38%
- ViT-B/32 (inference): 82.1% vs. 99.51%
- Gap is best explained by array-size tiling effect (64-MAC array tiles far more easily against
- these layer shapes than a 1024-PE array), not an architectural shortfall

## Slide 6
PrimeTime Synthesis Results -- Per-PE
TSMC 28nm, TT corner, 0.8V, 25°C
N (fusion width) | Clock period | Frequency | Area / PE | Power / PE
4 | 0.56 ns | 1.786 GHz | 11,302.58 µm² | 7.027 mW
8 | 0.64 ns | 1.5625 GHz | 15,147.97 µm² | 9.9077 mW
16 | 0.62 ns | 1.6129 GHz | 19,931.18 µm² | 15.080 mW
▸ N=8 to N=16: clock period improves slightly (0.64 -> 0.62 ns) despite doubling fusion width --
- opposite of the N=4->N=8 trend; reported as an observed synthesis result, not explained here
▸ Array-level (x1024 PEs): Area = 11.57 / 15.51 / 20.41 mm² | Power = 7.19 / 10.15 / 15.44 W

## Slide 7
Combined System-Level Results
SCALE-Sim cycles x PrimeTime PPA -- Table 1 summary
N | Peak TOPS | Achieved TOPS | TOPS / W | TOPS / mm² | Utilization
4 | 14.63 | 9.90 - 13.86 | 1.38 - 1.93 | 0.86 - 1.20 | 67.7% - 94.8%
8 | 25.60 | 17.33 - 24.26 | 1.71 - 2.39 | 1.12 - 1.56 | 67.7% - 94.8%
16 | 52.85 | 35.78 - 50.09 | 2.32 - 3.24 | 1.75 - 2.45 | 67.7% - 94.8%
▸ Ranges exclude the MLPerf-Transformer benchmark (documented outlier, slides 2 & 4)
▸ Wider fusion is a net win on every efficiency metric, not only raw throughput:
- N=4 -> N=16: power/PE grows 2.15x, area/PE grows 1.76x, peak throughput grows 3.61x
- net effect: TOPS/W improves 1.68x, TOPS/mm² improves 2.05x
▸ vs. published MX designs (Table 2, evaluation_methodology_paragraph.txt): competitive GOPS/W
- range at N=16 (2317-3244) against Cuyckens NPU-integrated work's 1438-1675 (MXFP8/6), one node behind